## Slide 1: Software for Embedded Systems
Prof. Saurabh Gandhi (EEE department)

## Slide 2: Where we are
Modeling  correct behavior by ensuring we have ‘thought’ of all possibilities
but not yet implemented!
Firmware architecture (so far)
  what pieces of code (loosely coupled, modules) do we need
  how these pieces control each other
What have we still not decided?
Application layer organization – how is the main logic implemented
When do these pieces of code run?

## Slide 3: Organization of the application layer
Application layer is the main (gooey) logic of your system; but within the app layer:
Is there a single controller that decides what to do next?
Are there multiple controllers?
Who receives events from the lower layers?
Who decides the mode or ‘state’?

## Slide 4: Pattern I: Monolithic controller
One central state machine that handles all state transitions and events

## Slide 5: Pattern II: Coordinated controllers
Separate state machines control therapy, alarm and UI
Coordination via defined interfaces

## Slide 6: Pattern III: Event dispatcher
One central dispatcher receives events
Separate controllers subscribe to events

## Slide 7: Event ownership at application level
Event | Owned By
Start button | Therapy Controller
Occlusion detected | Alarm Manager (may notify Therapy)
Timer tick | Therapy Controller
Low battery | Alarm Manager

## Slide 8: Comparison of application level patterns
Pattern | Strength | Weakness
Monolithic | Simple | Becomes large, mixed concerns
Coordinated Controllers | Clear separation | Ordering & coupling must be managed
Dispatcher | Modular & scalable | Indirect control flow
Property | Coordinated Controllers | Dispatcher
Who knows whom? | Controllers know each other | Controllers know only dispatcher
Direct function calls? | Yes | No
Coupling | Explicit, directional | Indirect, via event bus
Compile-time dependency | Strong | Weaker

## Slide 9: Control flow visibility
Coordinated Controllers
Control flow is explicit.
You can trace calls statically.
Easier to reason locally.
Harder to scale globally.
Dispatcher
Control flow is indirect.
Requires mental model of event routing.
Scales better.
Harder to trace.

## Slide 10: Ease of adding modules
Coordinated Controllers
Every new controller may require:
  new direct calls
  updated dependencies
  careful ordering
The dependency graph grows quadratically.
Dispatcher Pattern
New module:
  subscribes to events
  no other controller modified
The dependency graph remains star-shaped.
That’s the scaling advantage.
We want to add logging, safety monitor, UI refresh

## Slide 11: Final distinctions
Coordinated Controllers
Small system
Safety-critical clarity needed
Explicit authority required
Dispatcher
Large system
Many loosely coupled modules
Plugin-style extensibility
Question | Coordinated | Dispatcher
Who stops infusion? | Alarm calls Therapy directly | Alarm emits STOP event
Who routes events? | Caller | Dispatcher
Where is coupling expressed? | Function calls | Subscription list

## Slide 12: Where we are
Modeling  correct behavior by ensuring we have ‘thought’ of all possibilities
but not yet implemented!
Firmware architecture (so far)
  what pieces of code (loosely coupled, modules) do we need
  how these pieces control each other
What have we still not decided?
Application layer organization – how is the main logic implemented
When do these pieces of code run?

## Slide 13: Execution model = Rules of Running
An execution model defines how control flows through the system over time.
Where code runs (i.e. in what context)
When code runs?
CPU performs one task at a time.
We create the illusion of multitasking by switching Contexts
A context is the snapshot of the CPU’s soul: its registers, its program counter, and its stack
When we switch tasks, we "freeze" one soul and "thaw" another
Execution modeling is the management of CPU "Contexts" and the cost of switching between them

## Slide 14: Models and contexts
Superloop: everyone waits in a long line to run sequentially
Foreground/background: Loop + ISRs
Cooperative and preemptive multitasking
RTOS
Contexts:
Main loop
Interrupt
Task (RTOS)
Deferred work

## Slide 15: The superloop
Deterministic, simple
Context shared throughout
Hard to scale
Blocking breaks all timing constraints
Improvement: loop + ISR
Still sequential

## Slide 16: Multitasking
Illusion of parallel execution
No need to wait for something else to finish
Cooperative: tasks yield voluntarily to the next task
Preemptive: Scheduler starts and stops tasks
Idea of priority

## Slide 17: The cyclic executive model
Advantages
Simple implementation
  How would you implement?
Low overhead
Very predictable
Disadvantages
Cannot handle sporadic events
Everything must operate in lockstep
Code is scheduled manually
Solution: Cyclic executive with interrupts

## Slide 18: What do you do inside an interrupt service routine?

## Slide 19: Typical ISR
Copy peripheral data into a buffer
Indicate to other code that data has arrived
  How?
  Events
  Start or stop a process
  Change priority
Acknowledge the interrupt
  Tell the hardware that generated it that it has been handled
ISRs run fast!
Placed in RAM instead of flash
Leave longer reaction task outside the ISR

## Slide 20: CE + Interrupts
Extremely easy to implement
Very cheap also! No extra overhead code
But
Main loop running in lockstep
Programmer must handle scheduling
Scheduling is static (cannot dynamically change order of tasks)
Latency of event handling still long
Interrupts introduce jitter in task timing

## Slide 21: Cooperative multitasking
Processes relinquish control to other processes
More control on when a process stops and goes to another
  Better coordination between processes
Priority can be implemented by changing task order
  Simple scheduler that maintains priority queues
Programmer has to ensure a single process does not hog all CPU time
Bugs in a single task jeopardize all others

## Slide 22: Operating systems
Function and scheduling are usually orthogonal
Let programmer handle function
Operating system will handle the scheduling

## Slide 23: Operating systems for conventional vs embedded systems
Conventional:
Multiple threads or processes
File system
Virtual memory and paging
I/O and interrupt handling
Resource allocation
Command interface for executing programs
Embedded:
Lightweight threads
i/o and interrupt handling
Real time guarantees

## Slide 24: Embedded operating systems
Lightweight threads
Basic locks
Fast context switches
Input / output
API for talking to devices
Buffering
Interrupt handling
Translate interrupts to events handled by user code
Trigger new tasks to run
Real time guarantees
Guarantee that a task is called at a certain rate
Guarantee interrupt handling time
Priority or deadline driven scheduling

## Slide 25: Types of real time constraints
Hard – miss deadline, total failure of system. Minor or major disaster (people may die?)
Firm – result no longer useful after deadline missed
Soft – results gradually less useful as deadline passes.

## Slide 26: What factors make real-time hard?
Interrupts (timing disrupted by external event responses)
Unpredictability of CPU execution
  Branch prediction, caches, power modes and clock frequency changes, memory management (page fault)
Dynamic memory allocation and garbage collection
Unpredictable hardware (e.g. network access)
Operating systems (scheduler, context switching)
  So why do we use RTOSs?

## Slide 27: Real time operating systems
Low latency of OS calls
Fast context switching
Main goal: meeting task deadlines
Goal is not fairness (unlike conventional OSes)
If you have five homework assignments, and one is due in an hour, you will work on that one!

## Slide 28: RTOS Task Model
Each task a triplet: (execution time, period, deadline)
Execution time: how long the task takes to run
Period: how often the task must run
Deadline: relative to each period, when must task complete?
Usually: deadline = period
Can be initiated anytime during the period

## Slide 29: Periods can be very different for different tasks

## Slide 30: Can we have period (T) different from deadline(D)?
D < T (constrained deadline)
Control loops based on sensor data (T = 10 ms, D = 5 ms)
  Control must be applied early in each cycle
  Remaining time for actuation delay, communication etc.
In general
  Output must be produced early
  Downstream stages require time before next period starts
T < D (arbitrary deadline)
Logging / diagnostics (T = 50 ms, D = 100 ms)
  Logging is not urgent
  Batching improves efficiency
In general, when buffering is allowed

## Slide 31: Scheduling
Given a set of tasks, {(5, 10, 10), (2, 20, 8), (4, 10, 20)} how should they be scheduled to ensure deadlines are never violated?

## Slide 32: Fixed priority preemptive scheduling (FPPS)
Each task has a fixed priority
Always run the highest priority runnable process
Continue running till process ends or higher priority process appears
CPU
τ1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
τ2 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 2 | 2 | n0 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 2 | 2
τ3 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 0
0 | 1 | 2 | 2 | 3 | 1 | 3 | 2 | 2 | 1 | 3 | 3 | 2 | 1 | 2 | 0 | 0 | 1 | 2 | 2 | 0 | 1 | 2 | 2 | 3 | 1 | 3 | 2 | 2 | 1 | 3 | 3 | 2 | 1 | 2 | 0 | 0 | 1 | 2 | 2 | 0 | 1 | 2 | 2 | 3 | 1 | 3 | 2 | 2

## Slide 33: FPPS
What happens if you have multiple processes at the same priority?
Prohibit: each process has unique priority
Time-slice processes at the same priority
  Extra context switching
  No starvation within a priority level, everyone gets their turn
Processes at the same priority cannot preempt each other
  Less context switching, so more efficient

## Slide 34: Task sets do not always have a feasible schedule
Consider the task model:
P1 = (10, 20, 20)
P2 = (5, 9, 9)
Write down the appropriate priority levels that ensure these two tasks always finish in time
Is there any way these two tasks can be scheduled to meet all deadlines?
Not schedulable if tasks require more than 100% CPPU utilization!

## Slide 35: Rate Monotonic Scheduling (RMS)
Processes with shorter period given higher priority
Key result (Liu & Layland, 1973 JACM): RMS is optimal “If there is fixed priority schedule that meets all deadlines, then RMS will produce a feasible schedule”

## Slide 36: RMS example
For the tasks shown: p1 = (10, 20, 20); p2 = (15, 30, 30)
Is a schedule impossible?
Is RMS able to give the schedule?
Is any fixed priority able to give a schedule?
Does CPU utilization, U <= 1 guarantee feasible fixed priority schedule?
τ1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
τ2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
CPU

## Slide 37: When is there an RMS schedule?
U > 1: no schedule possible
RMS schedule always exists if U < n (21/n – 1)
If U < 69%, RMS will always give a schedule
If U > 69%, RMS may still give a valid schedule, but it is not guaranteed to work for all task models
RMS is optimal when T = D. When D < T: deadline monotonic

## Slide 38: RMS example
For the tasks shown: p1 = (10, 20, 20); p2 = (15, 30, 30)
No RMS schedule
For what model will a schedule exist?
p2 = (10, 30, 30) gives U = 83% (within limit for n = 2)
CPU
τ1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
τ2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2

## Slide 39: Can we do better with dynamic priorities?
Earliest deadline first
Process with the earliest next deadline given highest priority
p1 = (10, 20, 20); p2 = (15, 30, 30) (U = 100%)
τ1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Τ2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
CPU

## Slide 40: Earliest deadline first
EDF is optimal
  If a dynamic priority schedule exists, EDF will produce a feasible schedule
EDF is efficient
  A dynamic priority schedule exists if and only if utilization is no greater than 100%
  i.e. EDF is most efficient at getting every bit of CPU availability utilized

## Slide 41: Which is better – RMS or EDF?
Scheduling overhead:
  RMS: simple lookup of priorities: o(1)
  EDF: sort tasks based on deadline every time: o(n)
Analysis:
  RMS, with fixed priorities, is easier to analyze and debug for a system; more predictable
Overload behavior (if more U than supported):
  RMS: Low priority tasks suffer, high priority are always safe
  EDF: All tasks are knocked off deadline

## Slide 42: Priority inversion