## Slide 1: Software for Embedded Systems
Prof. Saurabh Gandhi (EEE department)

## Slide 2: Building a multitasking embedded software system
Multitasking introduces:
Concurrent execution
Shared data
Asynchronous events
Race conditions
Inconsistent state of the system
Need for synchronization and inter process communication (IPC)

## Slide 3: Race conditions

## Slide 4: Race conditions
What problem do you foresee with this code?
Multiple correct operations
But depending on timing / order, result can be incorrect / non-deterministic

## Slide 5: Inconsistent system state

## Slide 6: How do we avoid these?
Problem areas:
Data exchange  IPC
Safe access / ordering  Synchronization
Communication paradigms:
Shared memory
Message passing

## Slide 7: Shared memory
Problematic – race condition possible
Critical section
Limit access of shared memory ( / resource) to only one task at a time
Mutex
Binary lock to ensure resource is not used by other processes

## Slide 8: Mutex example
Shared resource
Initialize the mutex for this resource
Producer task

## Slide 9: Mutex example
Producer task
Consumer task

## Slide 10: Message passing
Message = type + payload
Queue = buffer for messages + pointers to head and tail + queue size
Initialization of a queue
Adding an item to the queue

## Slide 11: Message passing
Adding an item to the queue
Receiving an item from the queue

## Slide 12: Message passing

## Slide 13: Example – Event Driven Systems
System reacts to events
Event producer process must communicate with event consumer
Events placed in queue
Tasks consume events
Decouples producers and consumers
Supports asynchronous systems

## Slide 14: Shared memory vs message passing
Feature | Shared Memory (with Mutex) | Message Passing
Speed | Maximum (zero-copy) | Slower (copy overhead)
Safety | High risk of race conditions | Safer, encapsulated data
Synchronization | Explicit (Mutex/Semaphore) | Implicit (Send/Receive)
Topology | Single system only | Distributed/Multi-processor
Kernel Role | Setup only | Involved in every transfer

## Slide 15: Practical guidelines
Keep critical sections short
Prefer message passing for complex systems
Use bounded queues
Avoid nested locks
Use priority protocols